## Slide 1
GridLock
Event-Driven Congestion Forecasting
PS2 · Flipkart × Bengaluru Traffic Police
Prototype Round 2 Submission
8,171
Incidents analysed
47
Leakage-safe features
3
Prediction targets

## Slide 2
THE PROBLEM
Bengaluru loses hours to reactive traffic management
🚦
8,171 incidents (Nov 2023–Apr 2024)
Rallies, VIP movement, construction, breakdowns across 22 corridors
📋
Deployment is experience-driven, not data-driven
Officers decide resource allocation without any quantified impact estimate
⏰
Impact is unknown until the jam forms
A tree-fall or planned rally is not quantified until it has already disrupted traffic
🆘
No decision support at report time
Officers on the ground receive the call with no forecast, no recommended action

## Slide 3
Predict impact the moment an incident is reported
T1 ROAD CLOSURE RISK
Will this close the road?
3.74×
PR-AUC lift vs. baseline
XGBoost + isotonic calibration
100% planned-event recall
Calibrated probabilities
T2 DISPATCH PRIORITY
High or Low priority?
0.916
corridor-blind F1
Rule-validated + corridor-blind
Works on any road, not just
designated corridors
T3 DURATION BUCKET
How long to clear?
65.8%
bucket accuracy (vs 57.9%)
<1h · 1-3h · 3-8h · >8h
LLM estimates clearance from
officer note directly
→ Recommendation engine maps predictions to: manpower count · barricade count · diversion route · alert level · tow dispatch

## Slide 4
Three findings that separate honest ML from a hollow demo
LEAKAGE TRAP
(a)
End-point coordinates are a 98% proxy for closure
Of 689 incidents with an end-point, 676 (98%) required closure. The end-point is recorded because a closure happened — not known at report time. A naive model scores F1 0.98 and is meaningless. We ban all end-point and resolution-time columns.
DETERMINISM
(b)
Priority is a rule, not a prediction
priority = (corridor ≠ Non-corridor) with zero exceptions across 8,171 rows. We report this honestly and train a corridor-blind model (F1 0.916) that recovers priority from incident characteristics alone — enabling BTP to extend priority to any road.
ARTIFACT
(c)
Resolution time is partly a recording artifact
60% of records (vehicle_breakdown) are auto-modified at ~130 min regardless of real clearance. We re-frame T3 as bucket prediction (<1h / 1-3h / 3-8h / >8h) and identify which causes are predictable: accident=35 min MAE vs potholes=8,600 min.

## Slide 5
47 leakage-safe features — all computable at report time
🕐
Temporal
Hour, day-of-week, month
Refined peak: 11-12h & 16-19h
Weekend flag, night flag, hour bucket
📈
Past-only recurrence
Corridor / zone / grid / cause / veh-type
closure rates & incident counts
Days-since-last, city load (24h)
✖
Interaction features
planned_cause_risk = is_planned × cause_closure_rate
peak_cause_risk = is_peak × cause_closure_rate
corridor_cause_risk (product)
🤖
LLM text mining (Groq)
Severity 1-5 · lane blocking · vehicles
Tow/crane required · incident subtype
Estimated clearance minutes
⏱
Duration priors
Past-only mean clearance time
Per cause, corridor, zone
Past-only, no future leakage
📍
Spatial & flags
Lat / lon / distance to centroid
is_planned · is_heavy_vehicle
is_non_corridor · zone_missing

## Slide 6
RESULTS
Held-out chronological test set · n = 1,226 incidents
3.74×
PR-AUC lift (T1)
0.374 vs 0.086 baseline
0.836
ROC-AUC (T1)
strong discriminative power
1.000
Planned recall (T1)
every planned closure caught
65.8%
Bucket accuracy (T3)
vs 57.9% majority baseline
Target
Metric
Model
Baseline
T1 Closure
PR-AUC
0.374 (3.74× lift)
0.086
T1 Closure
ROC-AUC
0.812
0.500
T1 Closure
Planned recall
1.000
—
T1 Closure
Unplanned recall
0.532
—
T2 Priority
Weighted F1
0.9984
0.9984 (rule)
T2 Blind
Corridor-blind F1
0.916
—
T3 Bucket
Accuracy
65.8%
57.9%
T3 Bucket
1-3h class F1
0.800
—
T3 AFT
C-index
0.598
0.500

## Slide 7
Officer notes are the strongest single predictor
WHAT GROQ llama-3.1-8b-instant EXTRACTS
Severity score
1 (minor) to 5 (road blocked)
Blocking lanes
Does the note imply lane(s) blocked?
Vehicles involved
Count of vehicles mentioned
Requires tow / crane
Recovery equipment needed?
Incident subtype
vehicle_breakdown / collision / vip / crowd …
Estimated duration
LLM reasons: crane + truck → ~240 min
5,541
unique descriptions processed
~3.5 notes/sec
Groq batched API · 4 concurrent workers
✓ Handles English · Kanglish · Kannada script ✓ Rule-based fallback = 100% coverage ✓ #1 SHAP contributor for closure (T1) ✓ Multilingual — no translation needed

## Slide 8
From prediction to deployment plan in one call
EXAMPLE OUTPUT
Tree fall · Tumkur Road · 18:30
🔴
Alert level
CRITICAL
👮
Deploy
11 officers
🚧
Set up
11 barricades
↪️
Divert to
West of Chord Road
🏗️
Tow flag from note
Dispatch crane
⏱
Duration estimate
1-3h bucket
MANPOWER (2–16 officers)
base(priority) + closure_risk × 6 + severity + peak_hour + chronic_corridor + planned_event + lanes_blocked
BARRICADING (0–12)
Triggered: closure_prob ≥ 0.4 OR severity ≥ 4 OR lanes_blocked
Count = closure_prob × 8 + severity + 2 (if blocking)
DIVERSION ROUTE
Named corridor → alternate from dataset-derived corridor families:
Tumkur Rd → West of Chord · Mysore Rd → Magadi Rd · Hosur Rd → Bannerghatta Rd
ALERT LEVEL
CRITICAL: prob ≥ 0.6 or severity 5
HIGH: prob ≥ 0.35 or severity 4
MEDIUM: prob ≥ 0.15 or severity 3 LOW: otherwise

## Slide 9
The system improves with every closed incident
New incident
reported
T1 / T2 / T3
predicted
Deployment
recommended
Incident
closes
Features
updated
Model
retrained
← LEARNING LOOP
✅
Zero re-engineering needed
Recurrence features are past-only — re-running features → train on updated data automatically incorporates every new closed incident.
💡
Corridor-blind T2 enables expansion
F1 0.916 from incident characteristics alone. BTP can assign priority to new roads not yet classified as formal corridors.
⚠️
Data quality finding for BTP
Capturing a true 'road cleared' timestamp (not auto-modified record time) is the single biggest improvement BTP can make to unlock T3 accuracy.
📡
LLM cache grows incrementally
New officer note patterns improve duration estimates over time. Resume-safe — no re-processing needed for existing descriptions.

## Slide 10
LIVE DEMO +
REPRODUCIBLE PIPELINE
🔮 Predict & Recommend tab
› Enter: corridor, cause, vehicle type, datetime, officer note › Output: closure probability · priority · duration bucket › Deployment plan: officers · barricades · diversion route › Per-incident SHAP: why this forecast was made
📊 Insights tab
› Closure rate by cause / hour / corridor › Model metrics vs baselines (all 3 targets) › SHAP bar charts + calibration curve › The three data findings explained
pip install -r requirements.txt → python -m src.data_prep → python -m src.features → python -m src.train → streamlit run app/dashboard.py